SMAC RCCP-200

(OIL BASE RUST CONVERETERCUM FINISH PAINT )

Description

SMAC RCCP-200  is oil base rust converter cum finish paint with special nano anticorrosive agent to protect steel structure from atmospheric corrosion.

.

ADVANTAGES

Self priming

Rust converting

Excellent penetration and rust converting  on oil contaminated surface

Excellent performance even though poor surface preparation

Moisture tolerant and moisture release property after application of paint at the time of drying of paint

excellent corrosion resistance ( 1000 hrs salt spray )

moderate chemical resistant

Application  area

All types of ferrous steel structure

Drying time

Touch dry : 4-6 hr

Hard dry :  24 hr

Coverage : 5 sq.mtr /ltr/two coats

Thinning  : 20 %  by mto ,octanol,ketone

Packing : 4 ltr,20 ltr

Shelf life : 12  months in sealed container